## Slide 1: Lakeshore Telemetry Link: Protocol Specification

## Slide 2: 1 Status Report Formats
Three formats carry buffer status to the gateway. The short status report carries the status of one channel group in a buffer size field of 8 bits. The extended short status report also carries the status of one channel group, in a buffer size field of 11 bits. The long status report carries up to 23 channel groups, each in a buffer size field of 28 bits.

## Slide 3: 2 Header Fields
Every packet starts with the header fields of Table 1, in order. Each length field gives the length of the field that follows it.
Table 1. Header fields
Field | Length (bits)
Version | 13
Session ID Length | 14
Session ID | up to 173
Packet Number Length | 9
Packet Number | up to 36

## Slide 4: 3 Measurement Report
The measurement report contains, in this order:
– the serving cell index, 12 bits;
– the battery level, 24 bits;
– the received signal strength, 16 bits;
– the timing advance, 10 bits;
– the transmit power, 20 bits.

## Slide 5: 4 Link Failure Detection
A link failure is declared when any of the following conditions holds.
Condition 1: no acknowledgement is received within 856 ms.
Condition 2: 21 consecutive retransmissions fail.
Condition 3: the signal-to-noise ratio stays below 4.3 dB for 60 s.

## Slide 6: 5 Timers by Link State
When the link is congested, the following values apply.
The retransmission timer is 709 ms. The send window is 145 packets.
When the link is idle, the following values apply.
The retransmission timer is 1,245 ms. The send window is 180 packets.